## Slide 1: VHDL 7 Use of signals
In processes and concurrent statements

## Slide 2: Introduction
7.1 The use of signals in
  7.1.1 Signals and variables in concurrent statements outside processes.
  7.1.2 Signals and variables in processes
  7.1.3 combinational processes,
  7.1.4 clocked process
    (a) with asynchronous inputs
    (b) with synchronous inputs
7.2 Rules on multiple assignment of signals
7.3 Examples
Full text in “vhdl_additional1.doc”

## Slide 3: 7.1 The use of signals (overview)
Inside processes, they can be
  flip-flops, if clock triggering exists:
    E.g. if rising_edge(clk) is used
  combination logic , if no clock triggering exists
    E.g no if rising_edge(clk)
In processes: If multiple assignments occur to X
the last assignment “X <= ?“ overrides previous ones.
if rising_edge(clk)
if rising_edge(clk)

## Slide 4: Different cases of using signals
Signals
  In concurrent statements outside processes
  Inside processes
    Combinational processes – (no clock triggering inputs, all inputs should be in sensitivity list)
      Each “<=“ signal assignment is a combination logic
    Clocked processes: e.g. “If rising_edge(clk) is used
      Each “<=“ signal assignment is a flip-flop
      clocked processes with synchronous inputs ( syn. inputs should not be in sensitivity list). Process()
      Clocked processes with asynchronous inputs (asyn. inputs must be in sensitivity list).
      Process ( clk, sensitivity list )
if rising_edge(clk)
if rising_edge(clk)

## Slide 5: 7.1.1 Signals and variables in concurrent statement outside processes.
In processes: If multiple assignments occur to X
the last assignment “X <= ?“ overrides previous ones.

## Slide 6: Signals and variables in concurrent statement outside processes.
library IEEE;
use IEEE.std_logic_1164.all;
----------------------------------------------------------
entity test11 is -- a typical vhdl program
port ( clk,in1,in2,reset: in STD_LOGIC;
out1,out2,out3,out_con1,out_con2: out STD_LOGIC);
end test11;
architecture test11_arch of test11 is
begin --Concurrent statements here
out_con1<=in1 and in2; -- concurrent statement
out_con2<=in1 or in2; -- concurrent statement
---- out_con2<= in2; -- multiple assignment to one signal (out_con2) is not allowed in tools
-- without resolved logic support.
----(1) clocked process with asynchronous inputs --------------------
clocked_process1:process(clk, reset) -- – clocked process with asynchronous inputs
-- must have a clock triggering condition inside
---clock and asynchronous inputs must be in sensitivity list
-- it allows asynchronous input signals, such as reset or load etc.
begin if reset='1' then out1<='0'; -- asynchronous Input reset
elsif clk='1' and clk'event -- the triggering point
then
out1 <=in1 xor in2; -- sync. Signals and expressions
end if;
end process;

## Slide 7: Signals and variables in concurrent statement outside processes.
architecture test11_arch of test11 is
out_con1<=in1 and in2; -- concurrent statement,
out_con2<=in1 or in2; -- concurrent statement,
  --They are concurrent.
  --Signals can be assigned multiple values if “resolved logic” is used, e.g. std_logic etc.”
E.g. 1. in the following example, the result is 1.
  Sig1<=’L’; -- weak low, concurrent statement
  Sig1<=’1’ – forcing 1, concurrent statement
E.g.2 in the following example, the result is ‘X’ unknown.
  Sig1<=’1’; --forcing high, concurrent statement
  Sig1<=’0’; -- forcing 0, concurrent statement
Variables can only live in processes. Variables are sequential, their values change intermediately.
Process()

## Slide 8: Exercise 7.a --s1 , s2 ,s3 , s4 , s5 , out1 , out2 are std_logic signals Hint : concurrent statements , No process( )
0 architecture test11_arch of test11 is
1begin
2 s1<=s2; -- ?? Sequential or concurrent statement _____
3 s3<=s4 or s2; -- ?? Sequential or concurrent statement _____
4 s3<=s5; -- allowed or not allowed ? _______
5 clocked_process1:process(clk, reset)
6 begin if reset='1' then s3<='0'; -- ?? Asyn or syn. Reset input __
7 elsif clk='1' and clk'event -- the triggering point
8 then
9 s3 <=s1 or s4; -- allowed or not allowed , what is s3 ? __
10 end if;
11 end process;

## Slide 9: 7.1.2 Signals and variables inside processes
In processes: If multiple assignments occur to X
the last assignment “X <= ?“ overrides previous ones.
Process()

## Slide 10: Signals and variables in processes. (see p80 of [1])
Variables are same as in a sequential program.
Signals in Combinational processes: (see combinational_process3)
  All input signals of a combinational process must be in the sensitivity list:
    a combinational process has no edge triggering
    all inputs must be in the sensitivity list, (If not, unusual things may happen, otherwise those not in sensitivity inputs cannot affect the output – it is not right)
  Multiple signal assignments in combinational process:
    only the last assignment inside the process is effective.

## Slide 11: 7.1.3 combination process
In processes: If multiple assignments occur to X
the last assignment “X <= ?“ overrides previous ones.
Process()
Combination:
No cock edge detection

## Slide 12: 7.1.3 combination process It is a process but no clock edge sensing so no flip flop
combinational_process3: process(in1, in2)
-- combination process: NO clock trigger condition inside
-- no (if clk='1' and clk'event) or ( wait until clock=’1’) etc.
-- All input signals must in sensitivity list,
-- otherwise result is not predictable.
begin --
out3<=in1 xor in2;
out3<=’1’;--out3 will always be ‘1’ but not “in1 xor in2”, because it is
-- the last signal assignment expression in a process
end process;
end test11_arch;

## Slide 13: 7.1.4 clocked processes
In processes: If multiple assignments occur to X
the last assignment “X <= ?“ overrides previous ones.
Process()
Combination:
cock edge detection
If clk='1' and clk'event

## Slide 14: Overview of signals in clocked process:
An edge expression must be the only condition of an ‘if’ or an ‘elsif’ statement.
In a clocked process, the statement “if clk= ‘1’ and clk’event; or wait until clk= ‘1’¨ is used for sensing the triggering clock “clk” input signal. The other signals in a clocked process can be classified into 2 types: (i) synchronous input signals, (ii) asynchronous input signals,.
Synchronous input signals in a clocked process (for D inputs of flip-flops) : Each “<=” under a clock condition is treated as a flip-flop –
  To avoid confusion, try not to put synchronous input signals in the sensitivity list,
  In fact, there is no effect even if you put synchronous inputs in the sensitivity list
Asynchronous input signals in a clocked process (they are not D inputs of flip-flops but rather RESET, LOAD inputs).
  Note that, such asynchronous inputs never exist in wait-until clocked processes.

## Slide 15: 7.1.4 clocked processes (a) clocked process with synchronous inputs
In processes: If multiple assignments occur to X
the last assignment “X <= ?“ overrides previous ones.

## Slide 16: clocked pure synchronous process without sensitivity list --
--Use “wait until clock” to write process
--(2) clocked pure synchronous process without sensitivity list ------
clocked_process2:process
-- clocked pure synchronous process without sensitivity list
-- inferring synchronous logic
--clocked process using wait until clock=’1’
--triggering expression wait-until must be the first expression,
--hence, all other signals of this process must be synchronous input signals.
--There is no room for asynchronous input signals
begin wait until clk = ‘1’; -- wait for positive rising edge
out2<=’0’; -- multiple assignment is ok, but this statement has no effect since out2 has another assignment later
out2<=in1 nand in2; --only the last assignment state for a signal (i.e. out2 here) counts
end process;
Use “wait until clock” to write process

## Slide 17: clocked processes clocked process with synchronous inputs (see clocked_process2 of the above example)
Synchronous input signals in a clocked process (for D inputs of flip-flops) : Each “<=” under a clock condition is treated as a flip-flop
  To avoid confusion, try not to put synchronous input signals in the sensitivity list,
  In fact there is no effect even if you put synchronous inputs in the sensitivity list
D
Q
Synchronous input
clock

## Slide 18: 7.1.4 clocked processes (b) clocked process with asynchronous inputs
In processes: If multiple assignments occur to X
the last assignment “X <= ?“ overrides previous ones.

## Slide 19: 7.1.4 clocked processes (b) clocked process with asynchronous inputs
library IEEE;
use IEEE.std_logic_1164.all;
----------------------------------------------------------
entity test11 is -- a typical vhdl program
port ( clk,in1,in2,reset: in STD_LOGIC;
out1,out2,out3,out_con1,out_con2: out STD_LOGIC);
end test11;
architecture test11_arch of test11 is
begin --Concurrent statements here
out_con1<=in1 and in2; -- concurrent statement
out_con2<=in1 or in2; -- concurrent statement
---- out_con2<= in2; -- multiple assignment to one signal (out_con2) is not allowed in tools
---- without resolved logic support.
----(1) clocked process with asynchronous inputs --------------------
clocked_process1:process(clk, reset) – clocked process with asynchronous inputs
-- must have a clock triggering condition inside
---clock and asynchronous inputs must be in sensitivity list
-- it allows asynchronous input signals, such as reset or load etc.
begin if reset='1' then out1<='0'; -- asynchronous Input reset
elsif clk='1' and clk'event -- the triggering point
then
out1 <=in1 xor in2; -- sync. Signals and expressions
end if;
end process;

## Slide 20: clocked process with asynchronous inputs (see clocked_process1 of the above example)
Asynchronous input signals in a clocked process (e.g. RESET, LOAD inputs).
  Note that, such asynchronous inputs never exist in wait-until clocked processes (synchronous clocked processes).
Reset load
D
Q
Asynchronous inputs
clock

## Slide 21: 7.2 Rules on multiple assignment of signals
Signals
  In concurrent statements outside processes
    If Multiple assignment occur: resolved by “resolved logic”
  Inside processes
    Combinational processes – (no clock triggering inputs, all inputs should be in sensitivity list)
    Clocked processes
      clocked processes with synchronous inputs ( syn. inputs should not be in sensitivity list)
      Clocked processes with asynchronous inputs (asyn. inputs must be in sensitivity list)
    In processes: If multiple assignments occur to X, the last assignment “X <= ?“ overrides previous ones.

## Slide 22: Signals and variables in processes: Multiple assignments
When a signal is assigned a value, the assignment does not necessarily take effect because the value of a signal is determined by the processes (or other concurrent statements) that drive it.
If several values are assigned to a given signal in one process, only the last assignment is effective. Even if a signal in a process is assigned, read, and reassigned, the value read (either inside or outside the process) is the last assignment value.
If several processes (or other concurrent statements) assign values to one signal, the drivers are wired together. The resulting circuit depends on the expressions and the target technology. The circuit might be invalid, wired AND, wired OR, or a three-state bus. See “Driving Signals” in Chapter 7, “Concurrent Statements,” for more information.
http://www1.pldworld.com/

## Slide 23: Exercise 7.b
1 Architecture x of y is
2 out2<= in1; --?? allowed or not allowed___________
3 --
4 clocked_process2:process
5 begin wait until clk = ‘1’; -- wait for positive rising edge
6 out2<=in1 nand in2; --?? Needed or not needed ______
7 out2<=in3; --?? allowed or not allowed, what is out2? _______
8 end process;
Use “wait until clock” to write process
out2, in1 , in2 , in3 are std_logic_ signals

## Slide 24: Exercise 7.c (part 1)
What are these processes p1,p2 (clocked or combinational ) and why?
Which are synchronous , asynchronous, combinational inputs?
How to add asynchronous reset to p1?
------------example 1: lig1_sr syn. reset bzased on lightA.vhd -----
library IEEE; -- ok for foundation1.5
use IEEE.std_logic_1164.all;
entity traffic is
port (out_light :out std_logic_vector( 2 downto 0);
-- out_light uses type out because no feedback requirement
inB: in std_logic ;----------*********
clock: in std_logic);
end traffic;------------------------------------------------
Architecture lightA of traffic is
type traffic_state_type is (s0, s1,s2,s3);
signal L_stateA: traffic_state_type;
begin
end case; end process; end lightA;

## Slide 25: Exercise 7.c (part2)
----------------------- p1 --------------------------------------------------------------------------
p1:process --exec.once when clock rises;the sensitivity list is empty,it implies only the clock will trigger the process
begin wait until clock='1'; --edged-clock triggering point
if inB='1' -- reset
then L_stateA <=s0;
else
case L_stateA is
when s0 => L_stateA<=s1;
when s1 => L_stateA<=s2;
when s2 => L_stateA<=s3;
when s3 => L_stateA<=s0;
end case; end if; end process; --to be continued , see next page
----------------------- p2 --------- convert L_statesA to out_light ----------------------
p2:process(L_stateA) -- combin. process
begin
case (L_stateA) is
when s0 => out_light <="100";
when s1 => out_light <="110";
when s2 => out_light <="001";
when s3 => out_light <="010"; …..

## Slide 26: Questions 7.d
State the differences between signals and variables in a VHDL program.
Discuss the rules applied to VHDL multiple signal assignment instructions in the following cases:
  Inside processes.
  Outside processes.

## Slide 27: Q 7.e
There are 4 states in a state machine: A, B, C and D. And the machine has an asynchronous RESET, a clock signal CLK and a 1-bit synchronous input signal INX. It has also a 2-bit output signal OUTX. The flow diagram is shown below. Write the complete VHDL program for the design.

## Slide 28: Q 7.e (continue)

## Slide 29: Question 7f
What are the differences between combination processes and clocked processes?
  Answer:
    1) _____________________________________________
    2) ______________________________________________
What are the differences between
  clocked processes with synchronous inputs and
  clocked processes with asynchronous inputs?
  Answer:
    clocked processes with synchronous inputs :
      1) _________________________________________
      2) _________________________________________
    clocked processes with asynchronous inputs :
      1) ________________________________________
      2) ________________________________________

## Slide 30: Conclusions
  Combinational processes (no edge triggering element “if clk=’1’ and clk’event” or “wait until clk=’1’”): all input signals must be in the sensitivity list. For multiple signal assignments, only the last assignment operator “<=” for a particular signal counts.
  Clocked processes (have edge triggering element “if clk=’1’ and clk’event” or “wait until clk=’1’ ”):
    Do not put synchronous input signals (D inputs to flip-flops) in the sensitivity list.
    All asynchronous inputs should be in the sensitivity list. Otherwise the result may not agree with the hardware implementation.

## Slide 31: Reference
[1] VHDL for designers by Stefan Sjoholm, Prentice hall
[2] VHDL reference manual of Xilinx-foundation